## Slide 1
Sensors & embedded systems
COURSE 01 · INTRODUCTION
Sensing the physical world
Most electronic systems exist to capture information from the real world — a keystroke on a computer, a temperature or a position on a connected object — and react to it.
Overview and use cases

## Slide 2
01
OVERVIEW
02
COMMON USE CASES
Sensors are everywhere around us
Temperature
Environment, devices, industrial processes
Humidity
Weather, agriculture, building comfort
Air quality
Pollution, CO₂ and particles, indoors and out
GPS
Locating and tracking an object
Accelerometer
Detecting movement and behaviours such as driving patterns

## Slide 3
01
OVERVIEW
03
CHOOSING THE RIGHT SENSOR
Same family, very different sensors
The application decides which characteristics matter. Compare sensors on five criteria:
Precision
How close a reading is to the true value
Operating range
The span of values it can measure reliably
Response time
How quickly it reacts to a change
Acquisition frequency
How many readings it delivers per second
Output format
Analog voltage or digital bus such as I²C, SPI or UART

## Slide 4
02
EXAMPLES
04
EXAMPLE: TEMPERATURE
The use case sets the precision
Processor monitoring
± a few °C
Goal: detect overheating
An error of a few degrees is acceptable
Weather monitoring
± 0.1 °C
Goal: record small, real variations
Readings must stay consistent across many sensors
Indicative orders of magnitude; meteorological stations typically target about 0.1 °C.

## Slide 5
02
EXAMPLES
05
EXAMPLE: ACCELEROMETERS
Speed requirements vary by orders of magnitude
Orientation detection
6 states
Up, down, left, right, front, back
A low acquisition rate is enough
Drone flight control
10 Hz → 1 kHz
Measures the full acceleration vector accurately
Reacts fast enough to compensate for gravity, wind and movement

## Slide 6
03
ARCHITECTURE
06
INSIDE A SENSOR
Sensors now process data before reporting it
Physical quantities are analog at the source: pressure, temperature, force, acceleration
Simple sensors expose them as a change in resistance, current or voltage, read by the processor
Integrating the ADC inside the sensor reduces noise and the transformations applied to the signal
A small dedicated block drives this conversion — a tiny processor, not user-programmable
New sensors embed real processing, even neural networks, so the host can sleep until an event matters
IIS3DWB10IS
one package
Sensing element
MEMS · 3 axes
ADC
analog → digital
Digital processing
filtering · FIFO buffer
ISPU
C code · neural networks
SPI / I3C · interrupt on event
Host processor
sleeps until woken
Simplified view. ISPU: intelligent sensor processing unit. Source: STMicroelectronics, IIS3DWB10IS product page.

## Slide 7
03
ARCHITECTURE
07
SENSOR TYPES
From raw signal to on-chip decision
Temperature
Light
ANALOG
The processor measures the signal
Output is a resistance or voltage; the MCU must convert it
Temperature
Accelerometer
DISCRETE DIGITAL
The sensor sends a value
Small PCB modules with built-in ADC; readings arrive over I²C or SPI
ST IIS3DWB10IS, with ISPU
SMART SENSOR
The sensor makes a decision
Runs filtering and neural networks inside; wakes the host only on events

## Slide 8
The RP2040
The microcontroller, its interfaces, and the setup we use in practical sessions.

## Slide 9
04
RP2040
09
OUR MICROCONTROLLER
The RP2040 runs every practical session
A low-cost microcontroller designed by Raspberry Pi, best known from the Raspberry Pi Pico board.
2
Arm Cortex-M0+ cores
133
MHz maximum clock speed
264
KB of on-chip SRAM; program stored in external flash
30
GPIO pins, 4 of them usable as analog inputs
Source: Raspberry Pi, RP2040 datasheet.

## Slide 10
04
RP2040
10
ARCHITECTURE
Two cores and flexible peripherals
Core 0
Cortex-M0+ · 133 MHz
Core 1
Cortex-M0+ · 133 MHz
DMA
moves data without the CPU
Bus fabric
connects cores, memory and peripherals
SRAM
264 KB · 6 banks
Flash interface
QSPI · external
USB 1.1
device or host
PIO
8 state machines
Peripherals
ADC · 4 inputs
I²C ×2
SPI ×2
UART ×2
PWM · 16 channels
Timers
Temperature sensor
30 GPIO pins
each pin selects which peripheral drives it
Simplified view. Highlighted: the interfaces we use in the practical sessions. Source: RP2040 datasheet.

## Slide 11
04
RP2040
11
INTERFACES
Four ways to talk to a sensor
A quick map for now — each interface gets its own session later.
ADC
4 inputs · 12-bit
Reads a voltage directly from an analog sensor
I²C
2 wires · SDA, SCL
Shared bus: many sensors, each with its own address
SPI
4 wires · SCK, MOSI, MISO, CS
Fast link, one chip-select line per device
Serial
UART · TX, RX
Point-to-point stream between two devices

## Slide 12
04
RP2040
12
PRACTICAL SESSIONS
One setup for every project
The topology stays the same; only the sensor interface changes.
HARDWARE
Sensor
Measures a physical quantity
ADC
I²C
SPI
Serial
changes
MICROCONTROLLER
RP2040
Reads the sensor, processes the data, streams the result
Partially vibe-coded
USB
serial
PC
Application
Reads the serial stream and plots the data
Vibe-coded

## Slide 13
Analog-to-digital conversion
How a continuous voltage becomes a number a microcontroller can process.

## Slide 14
05
ADC
14
ANALOG VS DIGITAL
An ADC turns a continuous voltage into numbers
Analog: continuous
Changes smoothly and can take any value in a range
Example: a sensor voltage varying between 0 V and a maximum
Digital: discrete
Only a finite set of values
The ADC samples the voltage and approximates each sample by a number

## Slide 15
05
ADC
15
CONVERSION QUALITY
Two parameters set conversion quality
Resolution
vertical precision
8-bit
256 values · 0–255
10-bit
1024 values · 0–1023
More bits → smaller steps, less quantization error
Sampling rate
horizontal precision
Samples/s
how often the voltage is measured
Faster sampling → fast variations are captured

## Slide 16
05
ADC
16
REFERENCE VOLTAGE
The reference voltage sets the scale
code = Vin / Vref × 255
8-bit code
input voltage
0
0 V
128
Vref / 2
255
Vref
Why not simply VCC?
VCC varies with battery level and supply conditions
If Vref moves, the same input gives a different code
Use a fixed reference, below the minimum expected VCC
What it means for the sensor
Its output must stay between 0 V and Vref
Outside this range, the signal must be adapted first

## Slide 17
05
ADC
17
ADAPTING THE SIGNAL
A voltage divider scales a voltage down
Vout = Vin × R2 / (R1 + R2)
Vin
Input voltage to scale
R1
Resistor connected to Vin
R2
Resistor connected to ground
Vout
Voltage between R1 and R2, sent to the ADC
EXAMPLE
5 V signal into a 3.3 V ADC: R1 = 22 kΩ, R2 = 33 kΩ → Vout = 3.0 V

## Slide 18
05
ADC
18
RESISTIVE SENSORS
A divider turns resistance into voltage
photoresistor
Many sensors change resistance, not voltage: a photoresistor (LDR) reacts to light
Use the sensor as one of the two divider resistors
Its resistance variation becomes a voltage variation the ADC can read
More light
light level
→
Lower RLDR
resistance
→
Higher Vout
ADC reading

## Slide 19
05
ADC
19
RP2040 ADC
One converter, five inputs
AIN0
GPIO26
AIN1
GPIO27
AIN2
GPIO28
AIN3
GPIO29
AIN4
Temp. sensor
→
Multiplexer
AINSEL picks one input
→
SAR ADC
12-bit · 48 MHz clock
→
RESULT register
latest value
FIFO · 4 entries
→ IRQ or DMA
Successive approximation: the input is compared bit by bit, from MSB to LSB
One conversion takes 96 clock cycles: 2 µs
Only one input is converted at a time
Source: RP2040 datasheet, section 4.9.

## Slide 20
05
ADC
20
RESOLUTION
Natively 12 bits, effectively about 8.7
8-bit
0–255
Optional: FIFO SHIFT keeps the 8 most significant bits. Saves memory with DMA.
12-bit
0–4095
The real hardware resolution. RESULT always holds 12 bits.
16-bit
0–65535
Not a hardware mode. MicroPython read_u16() rescales the 12-bit value.
10-bit
—
No 10-bit mode on the RP2040.
8.7
ENOB, measured
Effective Number Of Bits
ENOB: the resolution of an ideal ADC with the same noise and distortion. Here, 12 bits on paper behave like 8.7 in practice
Known DNL errors around codes 512, 1536, 2560 and 3584
Source: RP2040 datasheet, section 4.9.3.

## Slide 21
05
ADC
21
SAMPLING AND CONFIGURATION
Up to 500 kS/s, shared across inputs
500 kS/s
Maximum rate: 48 MHz ÷ 96 cycles
4 + 1
External inputs plus the internal temperature sensor
÷ N
With N inputs in round-robin, each gets 500 ÷ N kS/s
Single conversion
Start once, read RESULT when ready
Free-running
Continuous conversions; a clock divider sets the rate
Round-robin
Cycles automatically through the selected inputs
FIFO + DMA
Streams samples to memory without the CPU
Source: RP2040 datasheet, section 4.9.2.

## Slide 22
05
ADC
22
INTERNAL TEMPERATURE SENSOR
The chip can measure its own temperature
How it works
Measures Vbe , the voltage of a biased bipolar diode, on input AIN4
Typically 0.706 V at 27 °C
Falls by 1.721 mV per °C
Must be enabled first (TS_EN bit)
T = 27 − (V − 0.706) / 0.001721
Linear: −1.721 mV per °C, from −40 to 85 °C
Accuracy
No guaranteed accuracy: Vbe and its slope vary from chip to chip
User calibration is needed for accurate readings
Very sensitive to the reference voltage, which the RP2040 does not provide internally
1 LSB ≈ 0.8 mV ≈ 0.5 °C at 3.3 V: a coarse sensor
Sources: RP2040 datasheet, section 4.9.4; Raspberry Pi documentation.

## Slide 23
I²C communication
Many sensors on two wires: addressing, reading, configuring, and how fast it can go.

## Slide 24
06
I²C
24
WHY I²C
Several sensors share the same two wires
One bus, many devices: no dedicated lines per sensor
SDA carries the data, in both directions
SCL carries the clock that synchronizes the exchange
Example addresses shown for illustration; each device has its own address on the bus.

## Slide 25
06
I²C
25
SDA, SCL AND PULL-UPS
Pull-ups give the bus a defined high level
Devices never drive the line high: they can only pull it low
When no one pulls, the resistor brings the line back to a known high level
Without pull-up, an idle line floats : neither high nor low, so readings become random
Both SDA and SCL need one, typically a few kΩ (10 kΩ in the SHTC3 example)
Idle → line high
Talking → pulled low when needed
Pull-ups may also be built into a microcontroller or a sensor breakout board. Source: SHTC3 datasheet, section 4.

## Slide 26
06
I²C
26
PROTOCOL
Every exchange starts with an address
start
7-bit address · 0x70
R/W
data byte(s)
stop
Write
S
1
1
1
0
0
0
0
0
ACK
command or register → sensor
ACK
P
Read
S
1
1
1
0
0
0
0
1
ACK
measurement bytes ← sensor
ACK
P
sent by the RP2040
sent by the sensor
START: the controller takes the bus
Address + R/W bit: only the matching device answers; 0 = write, 1 = read
ACK: the receiver confirms each byte by pulling SDA low
Example: SHTC3, fixed address 0x70. Source: SHTC3 datasheet, section 5.1.

## Slide 27
06
I²C
27
TWO-WAY COMMUNICATION
An I²C sensor can be read and configured
Analog sensor
One direction only: the sensor outputs a voltage
The microcontroller measures it with its ADC
No way to change how the sensor works
I²C sensor
Read: the sensor sends digital bytes, not a voltage
Write: the controller sends commands or register values
Configure operating mode, resolution or sampling behavior
Bytes must be decoded using the sensor datasheet
SHTC3 EXAMPLE
Writing a command selects normal or low-power mode, sleep or wake-up
Source: SHTC3 datasheet, sections 5.2 and 5.3.

## Slide 28
06
I²C
28
READING THE SHTC3
One measurement takes four I²C exchanges
1
Wake up
0x70 W
0x35
0x17
wait ≤ 240 µs
2
Measure
0x70 W
0x7C
0xA2
wait ≤ 12.1 ms
3
Read
0x70 R
T MSB
T LSB
CRC
RH MSB
RH LSB
CRC
6 bytes received
4
Sleep
0x70 W
0xB0
0x98
saves power
T = −45 + 175 · ST / 216
ST: raw 16-bit value = (MSB × 256) + LSB
Example: 0x64, 0x8B → ST = 25 739 → 23.7 °C
CRC byte lets us detect transmission errors
Command 0x7CA2: normal mode, temperature first, clock stretching. Source: SHTC3 datasheet, sections 5.3–5.11.

## Slide 29
06
I²C
29
ARDUINO EXAMPLE
Reading the SHTC3 with Arduino
Wire is the Arduino I²C library: it drives the bus as controller
SDA and SCL on the Pico: GP4 and GP5 by default (Arduino-Pico core)
0x70 selects the SHTC3 on the bus
The SHTC3 has no temperature register: a write command starts the measurement, then we read 2 bytes
SERIAL MONITOR
23.71 23.74 23.70
#include <Wire.h>
const uint8_t ADDR = 0x70; // SHTC3 address
void cmd(uint16_t c) { // 16-bit command
Wire.beginTransmission(ADDR);
Wire.write(c >> 8); Wire.write(c & 0xFF);
Wire.endTransmission();
}
void setup() { Serial.begin(115200); Wire.begin(); }
void loop() {
cmd(0x3517); delay(1); // wake up
cmd(0x7866); delay(13); // measure, T first
Wire.requestFrom(ADDR, 2); // read T MSB, LSB
uint16_t raw = Wire.read() << 8 | Wire.read();
cmd(0xB098); // sleep
Serial.println(-45 + 175.0 * raw / 65536);
delay(1000);
}
Command 0x7866: normal mode, temperature first, no clock stretching. CRC not checked here. Source: SHTC3 datasheet, sections 5.3–5.11.

## Slide 30
06
I²C
30
BUS SPEED
Bus speed sets a theoretical ceiling
Standard mode
100 kHz
≈ 1.5 ms on the bus
~650
measurements / s, bus limit
Fast mode
400 kHz
≈ 0.39 ms on the bus
~2 600
measurements / s, bus limit
Fast mode plus
1 MHz
≈ 0.15 ms on the bus
~6 500
measurements / s, bus limit
One SHTC3 measurement ≈ 154 clock cycles: 4 exchanges, address, commands, 6 data bytes, ACK bits
Max rate ≈ SCL frequency ÷ bits exchanged per measurement
Bit count from SHTC3 datasheet Figure 7; speeds from Table 6. Bus time only: waiting for the sensor is not included.

## Slide 31
06
I²C
31
IN PRACTICE
The sensor, not the bus, sets the pace
At 400 kHz, the bus alone would allow ~2 600 measurements/s. But each measurement also waits for the sensor.
Normal mode
wake 0.24
bus 0.39
measure 12.1 ms
~80 /s
12.7 ms each
Low-power mode
wake 0.24
bus 0.39
measure 0.8 ms
~700 /s
1.4 ms each
I²C transfer
sensor busy measuring
Several sensors share the bus: the transfer time is split between them
While one sensor measures, the bus is free to talk to the others
Maximum times from SHTC3 datasheet, Table 5. Bar lengths not to scale for low-power mode.